## Slide 1
Case Study:
Gasoline Tanker Roll-Over
Initial Response Actions and Restoration
NH Route 101, Epping, NH
Chris Wood
New Hampshire Department of Environmental Services
Spill Response & Complaint Investigation Section
Notes: Good morning! Can everyone hear me okay?
My name is Chris Wood and it’s a pleasure to be here today
A little background on me – I’ve been an investigator with the Spill Response & Complaint Investigation Section at NHDES for a bit over 4 years now. Prior to this, I spent 6 years in private consulting working mostly on petroleum remediation sites and brownfields redevelopment projects, along with some petroleum storage facility design work and SPCC Plan development.
Today I’ll be presenting a case study about a gasoline tanker rollover on Route 101 in Epping, NH, and the successful Initial Response Actions and Restoration work that has occurred to date.
I’ll talk about the emergency response and site stabilization actions taken, the coordination between multiple affected parties, the remedial action plan development and permitting, and then I’ll go over the site preparation, excavation, and restoration work.
I’ll wrap up with a brief summary of the results of the excavation, and then I’ll take questions about the project if you could please hold them until the end.

## Slide 2
December 16, 2019
Notification from NH State Police received 8:20pm
  “Gasoline gushing out like an open fire hydrant”
  11,000-gallon capacity
  Multiple Fire Departments on scene
  Emergency Response Contractor dispatched
  Spill into wet wooded area
Notes: On December 16, 2019, I was enjoying a rather peaceful night serving as the on-call DES responder. At 8:20pm, I received the adrenaline-inducing notification from New Hampshire State Police Dispatch of a tanker rollover on Route 101 in Epping with “gasoline gushing out of it like an open fire hydrant”. Dispatch indicated that the tanker capacity was 11,000 gallons, Multiple fire departments were on scene, and an Emergency Response Contractor had already been dispatched by the Responsible Party.
After jumping in my response vehicle, I contacted the State Police Sgt on-scene who indicated that the tanker was on its side and leaking into a wet wooded area but couldn’t provide much additional information (he was keeping a safe distance). I called the safety director for the Gasoline Hauler to discuss the incident and what actions they were taking. After already hiring a Response Contractor, the hauler dispatched one of their own empty tankers for gasoline recovery – this was good forward thinking, and they had rather expertly executed their response protocols. I touched base with the Response Contractor supervisor heading to the scene to discuss some initial strategies and equipment procurement, like a tanker truck to recover spilled gasoline and air monitoring equipment.

## Slide 3
Notes: Dec 16, 2019
This was the scene I arrived to. You can see the rear-end of the truck here, and obviously the tanker on its side. There were 3 or 4 charged fire hoses on standby in case this went south, and AFFF firefighting foam had been applied to reduce the risk of fire. At this point, gasoline was still leaking out of the rear-most hatch of the tanker. What you can’t see here is the >100 personnel on scene behind me with 10-12 fire trucks

## Slide 4
Challenges out of the gate
Highly flammable liquid with low S.G. into wetland area
Night operations - low visibility
Below freezing temperatures
Snowstorm forecast to begin in ~10 hours
>100 personnel on scene
Notes: Dec 16, 2019
Gasoline had begun to pool at the toe of the roadway embankment, and you can see the AFFF floating on the pools. The pool seemed to be migrating to the east, indicating the grade in the generally flat section of woods.
*CLICK*
Right out of the gate we knew we faced some challenges.
There was a large volume of a highly flammable liquid with a low specific gravity released into a wet area of woods
It was night-time, so there was going to be low visibility on scene throughout the extended clean-up operation
This was mid-December, so we were in below-freezing temperatures, and to make things interesting there was a large snowstorm forecast to begin in ~10 hours.
There were >100 personnel on scene, including:
  Several fire departments with 10-12 apparatus’ on scene, including a Striker Truck from the Pease Air National Guard Fire Department
  Members from the Seacoast HazMat Response Team
  The NH Fire Marshall
  The NH DOT District Engineer
  A Towing Company with several trucks
  The Cleanup Contractor hired by the RP
  And representatives from the Responsible Party

## Slide 5
Objectives determined with Incident Command
Scene safety – PREVENT FIRE
Remove truck from crash scene
Assess tanker and pump out remaining gasoline
Remove tanker from crash scene
Assess impacts and potential migration
Recover pooled gasoline
Stabilize scene and clear road before snow storm
Notes:   The scene was being run by an off-site Incident Command located down the road. The first and foremost objective established with the Incident Command was personnel safety - Fire must be prevented. It was directed that AFFF foam be applied to any exposed pools of gasoline to reduce flammable vapor production. Once it was deemed safe, the damaged truck would be removed from the scene first. Following truck removal, Incident Command would allow for personnel to approach and assess the damaged tanker to determine remaining contents and a pump-out strategy. Once the tanker was empty, it could then be dragged up the embankment and cleared from the scene. After the scene was cleared, the Response Contractor would be allowed to enter the spill area for product recovery and site stabilization work. Incident Command directed that operations needed to wrap up and the roadway cleared before the forecasted snow storm the following morning.

## Slide 6
Notes: Dec 16, 2019
With the help of firefighters, the Tow Company was able to drag the truck up the embankment. The damage was significant, but amazingly the diesel fuel saddle tank on this truck was virtually untouched.

## Slide 7
Tanker Recovery and Assessment
Significant damage to front headwall of tanker
Piping and valve gallery intact
Did not tap into tanker due to flammability – opened hatches front to back
Interior baffles compromised
Recovered ~4,500 gallons of virgin gasoline from rear compartment
  Estimated ~6,500 gallons released to the ground
Notes: Dec 16, 2019
Before allowing personnel to approach the tanker, more AFFF was applied to the spill area. At this point the leak from the rear hatch had stopped.
*CLICK*
Upon inspection, it was obvious that the majority of the release came from two large ruptures at the front headwall of the tanker. Interestingly, the all of the piping and valves beneath the tanker were seemingly intact. Instead of tapping into each of the 4 compartments of the tank, it was decided to open the hatches from front-to-back to look inside. Most of the interior baffles and compartment walls had been compromised. The Hauler worked with the Cleanup Contractor to recover about 4,500 gallons of gasoline from the rear-most top hatch of the damaged tanker. This gave us an estimated release volume of 6,500 gallons of gasoline to the ground.

## Slide 8
Notes: Dec 16, 2019
Here is a close-up of the damage to the front headwall of the tanker. This tanker rolled at least two times

## Slide 9
Notes: Dec 16, 2021
After the tanker was emptied, the Tow Company was able to drag it out of the woods and up the embankment to prepare it for transport off-site.

## Slide 10
Spill Assessment
Communication with IC for entry into “hot zone”
Generally flat wooded area filled with hummocks and dips containing exposed groundwater
Gasoline migrating through hummocks and held up by high water table
Stream located ~200’ north and ~350’ east of the release area
15+ gallons of AFFF concentrate applied to crash site
  Some class B foam
Notes: After the tanker was removed, Incident Command allowed for additional personnel to approach the spill site to begin assessment and recovery work. Prior to entry, additional AFFF foam was applied to the area and charged fire hoses remained on standby. Personal air monitoring equipment was used to determine Lower Explosive Limit and VOC concentrations as entry occurred. Personnel going down-range donned Level C PPE with respirators.
The terrain was found to be generally flat with a slight grade from west to east as indicated by gasoline flow direction. The woods were filled with small hummocks and dips, some of which contained exposed groundwater. A stream was found located about 200’ north and 350’ east (down-gradient) of the release area. Gasoline was pooled up to 2-feet thick in the source area, and had begun to migrate from the source area on the groundwater table, through the hummocks.
It was determined that 15+ gallons of AFFF concentrate was diluted into firefighting water and applied to the spill area; some of that was Class B foam. Upon initial assessment, the impacted area appeared to be about 40’ wide by 100’ long, and spreading.

## Slide 11
Gasoline Recovery and Scene Stabilization
Contractor recovered ~2,300 gallons of pooled gasoline from the ground into tanker
  Estimated ~4,200 gallons remain on the ground
Containment boom placed in two 1’-deep interceptor trenches on the east and west sides of the release
  Hand-dug with non-sparking tools
Roadway cleared at ~5:00am on December 17
Notes: After the extent of impacts had been determined, the Response Contractor used a tanker pump to recover about 2,300 gallons of pooled gasoline from the source area. This left about 4,200 gallons of gasoline in the surrounding soil. While the recovery was ongoing, we began to hand dig two interceptor trenches with non-sparking tools – one on either side of the release area – that intersected the water table. Containment boom was placed in the trenches to help prevent the migration of gasoline beyond those points. By the time the large pools of gasoline were pumped out and the interceptor trenches established, the snowstorm was imminent and Incident Command determined it was an appropriate time to clear the scene at about 5:00am.

## Slide 12
Ongoing Stabilization and Recovery Work
SAFETY – Side of Roadway, Gasoline vapors
Contractor continued pumping pooled gasoline from source area and surrounding area
Determined the extent of impacts and migration path of gasoline
Absorbent pads and boom deployed in exposed pools of gasoline
Large interceptor trench excavated east of the release area, down-gradient of impacts
Notes: A day later, on December 18, after the roadway had been cleared of snow, the Response Contractor returned during daylight hours and we delineated the extent of gasoline impacts in the woods. The local Fire Department was present with a charged hose on standby, and NH State Police assisted with a shoulder closure. Several laborers were on scene to apply absorbents to exposed gasoline that was exposed in low areas. Another tanker truck was used to recover pooled gasoline from pockets dug in and around the source area. The hand-dug interceptor trench to the east of the spill area had lost its effectiveness due to a drop in the water table, allowing gasoline to pass beneath the containment boom.
On December 19, a large interceptor trench was excavated in clean soil/groundwater down-gradient of the release area to the east using a mini-excavator. The trench extended from the toe of the slope to the edge of the NH DOT right-of-way, and was equipped with both absorbent and containment boom to prevent migration.

## Slide 13
Notes: Dec 20, 2019
Here is a view of the large pool at the source area where the tanker was located. The Response Contractor was able to recover much of the spilled gasoline as it recharged this low point.

## Slide 14
Notes: Dec 19, 2019
The response contractor applied absorbent pads to exposed pools of gasoline in the woods. The extent of impacts had spread to about 50’ wide by 250’ long by this point, about 36 hours after the spill.

## Slide 15
Notes: Dec 20, 2019
This is the interceptor trench that was dug using the mini-excavator, about 300’ down-gradient of the source area, which was much more effective than the hand-dug trench. The source area is located to the right of this photo. Just hours after installing the boom, sheen was observed migrating into the trench from the spill. - it was critical to get that in place before timing.

## Slide 16
Coordination Meeting and Planned Work
Responsible Party (Hauler), Insurance Rep, Consultant, Response Contractor, Local FD, Local DPW, NH DOT, NH DES
Input from NH DOT for roadwork and restoration requirements
NH DES: Env-OR 600 requires clean-up meeting SRS and AGQS
Input from Response Contractor regarding work practices
Input from Consultant regarding remediation strategy
Notes: Now that we had a handle on the scene, NH DES held a coordination meeting with the affected parties. Present for the Responsible Party was their Safety Director, an Insurance representative, their Consultant, and the Response Contractor. The Local Fire Chief was present, along with a rep from the Local DPW. NH DOT was present to discuss roadwork safety and restoration requirements. NH DES outlined the clean-up requirements of meeting the Soil Remediation Standards and Ambient Groundwater Quality Standards listed in the Env-OR 600 rules. The Response Contractor provided input on work practices, and the Consultant on investigation and remediation strategies. It became a collaborative discussion on the safest and most efficient way to remediate the site.

## Slide 17
Remediation Challenges
Hand work required until flammability hazard is removed
  Local FD Fire Watch at scene on standby
Access to site – clear trees and build ramps down to work pad next to spill
High water table presents disposal challenge
  Dewater stockpile prior to load-out
Wetland area requires delineation for appropriate restoration
  Emergency Authorization – NH DES Wetlands Bureau
Notes: We faced a few unique challenges to remediate this site. Most notably was the flammability hazard, which meant that handwork with absorbents and pumping was required until the hazard was eliminated (vapors reduced). The Local Fire Department coordinated fire watches during working hours with surrounding mutual aid stations. Access to the site was the next largest challenge. Trees would need to be cleared after the flammability hazard was mitigated, then ramps would need to be built down to a work pad located just up-gradient of the spill area. During excavation, the high water table was going to present a disposal challenge, so a stockpile dewatering area was to be incorporated into the work pad. Based on the terrain, vegetation, and water table, the NH DES Wetlands Bureau was to be notified and would provide an Emergency Authorization for the tree removal and soil-disturbing work.

## Slide 18
Remedial Action, Road Safety, and Restoration Plans
Remedial Action Plan in accordance with NH DES Env-OR 600
  Outlines remediation/excavation plan and endpoint sampling strategy
  Remedial Action Plan Completion Report to be submitted at completion
Wetlands Delineation and Restoration Plan required by NH DES
Road Safety Plan in accordance with US DOT rules
  Jersey barriers, crash arrestors, and warning signage
Excavation Permit required by NH DOT
  Entry/exit ramp and work pad construction procedure/specs
Notes: The Consultant really had their work cut out for themselves at this point. A Remedial Action Plan was required in accordance with Env-OR 600 to outline the planned excavation and restoration work and a Wetlands Delineation and Restoration Plan was to be submitted for review and approval. NH DOT required a Roadwork Safety Plan and an Excavation Permit to install safety barriers and crash arrestors along the shoulder of Route 101 to construct the ramps, work pad, and completed the excavation work.

## Slide 19
Notes: Jan 14, 2020
While the Remedial Action and Roadway Safety Plans were being developed and permits issued, the Response Contractor continued absorbent application and pumping work at the site. You can see the large pile of bagged spent absorbents here

## Slide 20
Notes: Jan 14, 2020
The Response Contractor began manually cutting and collecting gasoline-impacted brush and trees. They dug small holes all over the area where free product could be pumped and allowed to recharge – the grade stakes marked the holes

## Slide 21
Notes: Jan 24, 2020
Local Fire Departments were present and on standby during the first several weeks of work while ignitability from free product and impacted soil was a concern.

## Slide 22
Notes: Jan 24, 2020
When vapor levels low enough for machine work to begin, the Response Contractor began removing some of the medium-sized trees with the mini excavator. The larger trees were left to be removed by a tree service or logging company due to their height and proximity to Route 101.

## Slide 23
Notes: Feb 4, 2020
The proposed work pad area up-gradient of the spill site was cleared first to allow for larger equipment to be mobilized to the site.

## Slide 24
Notes: This was part of the Roadwork Safety Plan and Work Pad Construction Plan developed by the Consultant. It outlined the installation and layout of the various roadway crash protections and the specifications for the construction and restoration of the roadway embankment ramps. The Remedial Action Plan prepared by the Consultant outlined excavation down to or just below the water table, guided by soil headspace sampling using a photoionization detector. End-point excavation samples were to be collected periodically and sent for laboratory analysis of VOCs, TPH-GRO, and PFAS.

## Slide 25
Notes: Feb 4, 2020
A sub-contractor familiar with roadwork was brought in to install the crash protection devices. You can see one of two wind socks that were installed early on in the project to monitor wind direction for gasoline vapor issues, which had been mitigated by this point.

## Slide 26
Notes: Feb 14, 2020
This was mid-February, so just a little over two months after the crash. The crash protections have been installed, the ramps and work pad have been constructed (and covered in snow), and much of the site tree clearing had been completed at this point.

## Slide 27
Notes: Feb 14, 2020
This was the stockpile dewatering area at the edge of the work pad. In the back you can see that erosion controls were installed around the work zone during work pad construction.

## Slide 28
Notes: Feb 20, 2020
This photo shows the site being cleared and prepared for excavation.

## Slide 29
Notes: March 9, 2020
Sand was brought in to stabilize the ground to load and transport excavated soil to the stockpile dewatering area.

## Slide 30
Notes: March 9, 2020
Excavation began at farthest down-gradient point and was advanced down to or just below the water table. There was sporadic minimal sheen observed on groundwater.

## Slide 31
Notes: Mar 19, 2020
The excavation progressed quickly because it was not very deep. The spring thaw added some water to the site

## Slide 32
Notes: April 22, 2020
This photo shows the completed, and flooded, excavation. The interceptor trench is visible in foreground

## Slide 33
Notes: Apr 29, 2020
A week later, after the results from the final excavation-endpoint soil samples were received, backfilling began with stone and gravel.

## Slide 34
Notes: Sept 1, 2020
This photo shows the bulk of the backfilling complete and just waiting for final loam and seed and wetlands restoration. To assess groundwater quality in the source area and surrounding the excavation area, the Consultant installed a network of monitoring wells within the source area and surrounding the site for groundwater monitoring. The locations of the monitoring wells were coordinated with NH DES.

## Slide 35
Notes: Oct 15, 2020
Only a small portion of the site was delineated as wetland. The Response Contractor installed some really nice red maples and shrubs per the approved Wetlands Restoration Plan.

## Slide 36
Notes: I thought this was a neat visual – here is a Before aerial image of the accident site.

## Slide 37
Results of Excavation
Excavated and disposed of 3,373 tons of impacted soil
  Not including trees, stumps, and absorbents
Recovered ~6,900 gallons of gasoline and gas/water mix
Collected 19 post-excavation soil samples
  -Excavation mostly affective, low-level SRS violations in a couple locations along roadway embankment (excavation limited by roadway)
Notes: And here is the After image at the same scale.
In total, 3,373 tons of gasoline-impacted soil was excavated from the site and sent off for landfilling. 6,900 gallons of gasoline and gas/water mix were recovered from the site. 19 post-excavation samples showed that most of the impacts were removed, with the exception of some low-level Soil Remediation Standard violations along the edge of the roadway embankment. The roadway embankments could not be disturbed much, per NH DOT. At the completion of the project the work pad, access ramps, and crash protections were removed.

## Slide 38
Groundwater and Surface Water Monitoring Results
GW monitoring:
  -Low-level AGQS violations for select VOC’s in source area wells
  -PFAS detected in source area wells and at down-gradient wells (<AGQS)
SW monitoring:
  -3 repeatable sample locations in nearby unnamed stream
  -No petroleum detections
  -PFAS concentrations detected at down-gradient location
Two rounds of groundwater sampling show similar results
(June & July 2020)
Notes: 10 Monitoring wells were installed and two rounds of samples were collected for laboratory analysis. The results indicated that select VOC’s were present at concentrations above the Ambient Groundwater Quality Standards in the source area only. Select PFAS compounds were detected in source area and in downgradient wells, but at concentrations below their applicable AGQS. Surface Water samples were collected from repeatable locations along the stream located north and east of the site. No petroleum, compounds detected, but some PFAS compounds were detected in the down-gradient surface water sample location. I will note that there currently are no surface water standards for PFAS compounds.

## Slide 39
Future Investigation and Remediation
At completion of Initial Response Action phase, the project is passed to the NH DES Petroleum Remediation Section for management
Additional groundwater and surface water monitoring requested
Additional groundwater investigation required
SRS violations in roadway embankment to be addressed
Notes: After the Initial Response Action phase of excavation and restoration was completed, project management at NH DES shifted from Spill Response to the Petroleum Remediation Section for additional monitoring and investigation work. Additional rounds of groundwater monitoring have been requested by NH DES, and the SRS violations that remain along the roadway embankment will need to be addressed.

## Slide 40
Special Thanks
First Responders
JP Noonan
St. Germain
Clean Harbors Environmental Services
Notes: Before I open up for questions, I wanted to take the chance to give a few shout-outs. First, a thank you to all of the first responders who showed up that night and prevented a catastrophic fire from erupting. We do a lot of business with them and they work hard to keep us safe. JP Noonan stepped up to the plate right out of the gate to make sure that clean-up efforts began immediately, despite the accident not being their driver’s fault. St. Germain did a lot of work coordinating with two state agencies, the contractor, and the RP to get the clean-up completed. But I think Clean Harbors had the hardest job – the foreman and laborers spent their winter and spring dealing with a messy gasoline spill in a pretty wet area right alongside a busy roadway.

## Slide 41
Questions?
Chris Wood
NH Department of Environmental Services
Waste Management Division
29 Hazen Drive, PO Box 95
Concord, NH 03302-0095
Christopher.B.Wood@des.nh.gov
(603) 271-3746
Notes: With that, here is my contact information, and I’ll open the floor to questions.